## Slide 1: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS
Presenter:
Michael Fetick

## Slide 2: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Agenda Introduction Choices of Network Protocols Early Network Protocols Today’s Wired Network Protocols Today’s Wireless Network Protocols Conclusion References

## Slide 3: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Introduction What are Network Standards (Protocols)? Rules that govern the exchange of messages between hardware and software processes on different computers, including messages (ordering, semantics, and syntax), reliability, and connection orientation.

## Slide 4: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Choices of Network Protocols The first choice in a network design is the topography. The most common network protocols are: - Ethernet, - Local Talk, - Token Ring, - FDDI, - ATM

## Slide 5: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Early Network Protocols

## Slide 6: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wired Network Protocols Ethernet Fast Ethernet Local Talk Token Ring FDDI ATM Gigabit Ethernet

## Slide 7: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wired Network Protocols Ethernet – By far the most widely used one. Ethernet uses an access method called CSMA/CD (Carrier Sense Multiple Access/Collision Detection). Each computer listens to the cable before sending anything through the network. If the network is clear, the computer will transmit. The computer will wait and try again when the line is clear. Sometimes, two computers attempt to transmit at the same instant and a collision. Each computer then backs off and waits a random amount of time before attempting to retransmit.

## Slide 8: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wired Network Protocols Fast Ethernet – A new standard that supports 100 Mbps but requires the application of different, more expensive network concentrators/hubs and network interface cards. Category 5 twisted pair or fiber optic cable is necessary. Fast Ethernet is becoming common in schools that have been recently wired

## Slide 9: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wired Network Protocols Local Talk a network protocol that was developed by Apple Computer, Inc. for Macintosh computers. The method used by Local Talk is called CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance). It is similar to CSMA/CD except that a computer signals its intent to transmit before it actually does so. Local Talk adapters and special twisted pair cable can be used to connect a series of computers through the serial port.

## Slide 10: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wired Network Protocols Token Ring protocol was developed by IBM in the mid-1980s and involves token-passing. A single electronic token moves around the ring from one computer to the next. If a computer wishes to transmit and receives an empty token, it attaches data to the token. The token then proceeds around the ring until it comes to the computer for which the data is meant.

## Slide 11: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wired Network Protocols FDDI is a Fiber Distributed Data Interface (FDDI) network protocol used primarily to interconnect two or more local area networks, often over large distances. The access method involves token-passing on a dual ring topology. If a break occurs, the system keeps information moving by automatically using portions of the second ring to create a new complete ring. A major advantage of FDDI is high speed over fiber optic cable at 100 Mbps

## Slide 12: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wired Network Protocols ATM is a Asynchronous Transfer Mode (ATM) network protocol that transmits data at a speed of 155 Mbps and higher. It transmits data in small packets of a fixed size. It supports a variety of media such as video, CD-quality audio, and imaging. ATM employs a star topology, which can work with fiber optic as well as twisted pair cable. ATM is most often used to interconnect two or more local area networks.

## Slide 13: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wireless Network Protocols Wireless Fidelity (Wi-fi) IEEE 802.11b IEEE 802.11a IEEE 802.11g

## Slide 14: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wireless Network Protocols Wireless Fidelity (Wi-fi) is a logo and term given to any IEEE 802.11 wireless network product certified to conform to specific interoperability standards. Wi-Fi certification comes from the Wi-Fi Alliance, a nonprofit international trade organization, which ensures that products will work with all other manufacturers’ Wi-Fi equipment on the market. By purchasing only devices bearing the Wi-Fi logo, you ensure that they will work together.

## Slide 15: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wireless Network Protocols IEEE 802.11b (Wi-Fi, 2.4 GHz band–compliant, Wireless-B) wireless networks run up to max. speed of 11 Mb/s, same as 10BASE-T Ethernet. They can connect to Ethernet networks or be an independent network. They use the same 2.4 GHz spectrum that many portable phones, wireless speakers, security devices, microwave ovens, and Bluetooth products use; although a potential source of interference, the short range of wireless networks (up to 150 feet indoors, 300 feet outdoors) minimizes the risks. The spread-spectrum method of connecting is used to minimize potential interference

## Slide 16: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wireless Network Protocols IEEE 802.11a (also referred to as Wireless-A) uses the 5 GHz frequency band allowing higher speeds (up to 54 Mb/s) and helps avoid interference from devices that cause interference with lower-frequency 802.11b networks. Although real-world 802.11a hardware seldom reaches that speed, it maintains its speeds at both short and long distances. Using the 5 GHz frequency instead of the 2.4 GHz frequency used by 802.11b/g, standard 802.11a hardware cuts itself off from the vast 802.11b/g universe.

## Slide 17: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Today’s Wireless Network Protocols IEEE 802.11g (Wireless-G) offers compatibility with 802.11b along with higher speeds. The final 802.11g standard was ratified in mid-2003; early 802.11g hardware was slower and less compatible than the specification promised. In some cases, problems with early-release 802.11g hardware can be solved through firmware or driver upgrades.

## Slide 18: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS Conclusion Just a few decades into the evolution of the Internet. As we advance through the 21st century, advancements in IPv6 will bring address capacity that can handle the connected, Internet of Things. Our society is a global scale, with our mobility increasing, we are exchanging ideas and concepts at a faster pace.

## Slide 19: EVOLUTION AND COMPARISON OF NETWORK PROTOCOLS References
Mueller, S. (Aug 2011). Upgrading And Repairing PCs (20th ed.). Que. Retrieved from http://www.tomshardware.com/print/local-area-network-wi-fi-wireless,reviews-3020.html Network Protocol - Types of Network Protocols. (2016, Feb 9). Retrieved from All-In-One Diagram Software for Flowchart, Org Chart and Mind Map: https://www.edrawsoft.com/Network-Protocol.php Panko, R. R. (2009). Business Data Networksand Telecommunications (7th ed.). Upper Saddle River, New Jersey: Pearson Education, Inc.

## Slide 20
Team Case Study: e-Commerce Success of Answers.com